## Slide 1
PolSARproSim+
Razi Ahmed
Jet Propulsion Laboratory, California Institute of Technology,
A summary

## Slide 2: Background
Based on PolSARproSim, which is a, coherent, fully polarimetric and interferometric SAR simulation of forest
Distributed by ESA, written in ANSI C.
HH
HV
VV
Coherence
Phase
Flattened Phase

## Slide 3: PolSARproSim+ SAR image
The SAR image is evaluated as a coherent sum of scattering events from small elements of the scene
Given the map of tree locations and dimensions a grid of points is used to sample the attenuation of the coherent wave in 3D

## Slide 4: Process flow

## Slide 5: Forest and Tree Description
A tree is realized in PolSARproSim+ based on primitives that include
  Location
  Height
  Canopy shape
  Canopy depth
  Canopy radius
  Stem Diameter
The fine structure of a tree is defined by species specific parameters for
  Stems
  Primary branches
  Secondary branches
  Tertiary branches
  Foliage

## Slide 6: Input forest description
Added the ability to read in forest primitives in the form of XML files
<?xml version="1.0" encoding="ISO-8859-15"?>
<?xml-stylesheet type="text/xsl" href="forest.xsl"?>
<forest>
<meta>
<num_trees units="none"> 470 </num_trees> <!-- The total number of trees in this file -->
<biome units="none"> temperate </biome> <!-- The biome this forest belongs to -->
<area units="ha"> 0.4604 </area> <!-- The total area of the forest -->
</meta>
<tree>
<species units="none"> ACRU </species> <!-- Pinus Resinosa, Red Pine (see allometry file) -->
<x_location units="meters"> -38.2800 </x_location> <!-- X-axis location of tree, scene center is 0.00 -->
<y_location units="meters"> -15.3100 </y_location> <!-- Y-axis location of tree, scene center is 0.00 -->
<tree_height units="meters"> 20.0000 </tree_height> <!-- Vertical extent from tree base to canopy top -->
<canopy_radius units="meters"> 2.0000 </canopy_radius> <!-- The largest horizontal radius of the canopy -->
<canopy_depth units="meters"> 3.1980 </canopy_depth> <!-- The depth of the live part of the canopy -->
<dry_depth units="meters"> 0.3107 </dry_depth> <!-- The depth of the dry part of the canopy -->
<stem_diameter units="meters"> 0.6840 </stem_diameter> <!-- Diameter of trunk at breast height (dbh) -->
</tree>
<tree>
<species units="none"> PIRE </species> <!-- Pinus Resinosa, Red Pine (see allometry file) -->
<x_location units="meters"> -37.7800 </x_location> <!-- X-axis location of tree, scene center is 0.00 -->
<y_location units="meters"> -16.9100 </y_location> <!-- Y-axis location of tree, scene center is 0.00 -->
<tree_height units="meters"> 25.5700 </tree_height> <!-- Vertical extent from tree base to canopy top -->
<canopy_radius units="meters"> 1.1100 </canopy_radius> <!-- The largest horizontal radius of the canopy -->
<canopy_depth units="meters"> 1.7820 </canopy_depth> <!-- The depth of the live part of the canopy -->
<dry_depth units="meters"> 0.3960 </dry_depth> <!-- The depth of the dry part of the canopy -->
<stem_diameter units="meters"> 0.8745 </stem_diameter> <!-- Diameter of trunk at breast height (dbh) -->
</tree>
.
.
.
.
</forest>
Azimuth
Range
Azimuth
Range

## Slide 7: Species description

## Slide 8: Stem angle
 | max polar angle
Left Tree | 30 degrees
Right Tree | 1 degree

## Slide 9: Stem tropism
 | Tropism theta | Tropism phi | Tropism factor
Left Tree | 180 | 0 | 0.8
Right Tree | 0 | 0 | 0.1

## Slide 10: Stem curvature
 | Gamma
Left Tree | 0.75
Right Tree | 0.0075

## Slide 11: Primary branch numbers
 | Layer density | Sections
Left Tree | 1.0 | 1
Right Tree | 4.01 | 6

## Slide 12: Primary branch angles
 | Polar angle
Left Tree | 50
Right Tree | 110

## Slide 13: Primary branch curvature
 | Gamma
Left Tree | 0.075
Right Tree | 0.75

## Slide 14: Primary branch tropism
 | Tropism theta | Tropism phi | Tropism factor
Left Tree | 0 | 0 | 0.3
Right Tree | 90 | 0 | 0.8

## Slide 15: Secondary branch numbers
 | Slope | Intercept
Left Tree | 1.045 | 0
Right Tree | 18.95864 | -4.26094

## Slide 16: Secondary start offset
 | Fractional offset [0-1]
Left Tree | 0.8
Right Tree | 0.3

## Slide 17: Secondary polar angles
 | Mean | Std dev.
Left Tree | 45 | 20.0
Right Tree | 7 | 0.65

## Slide 18: Secondary start radius factor
 | Radius Factor [0-1]
Left Tree | 0.1
Right Tree | 1.0

## Slide 19: Secondary branch tropism
 | Tropism theta | Tropism phi | Tropism factor
Left Tree | 0 | 0 | 0.0
Right Tree | 90 | 0 | 0.9

## Slide 20: Secondary branch curvature
 | Gamma
Left Tree | 0.075
Right Tree | 0.75

## Slide 21: Tertiary branch controls
Size (radius, length) are calculated based on primary and secondary branch dimensions. Although minimum dimensions can now be specified.
Tertiary volume fraction, canopy size, branch volume, and Maximum Number of realizations (for Monte Carlo purposes) decide the actual number of branches.

## Slide 22: Foliage controls
Can now specify mean/stdev of leaf dimensions

## Slide 23: Foliage controls
Leaf volume fraction, canopy size, leaf volume, and Maximum Number of realizations (for Monte Carlo purposes) decide the actual number of leaves.

## Slide 24: Modeling temporal decorrelation
PolSARproSim+ includes the option of modeling temporal decorrelation as change of scatterer position and moisture as a function of height, for each track
Moisture and Motion profiles are defined by programmable coefficients:
  No change
  Polynomial change profile:
  Exponential change profile:

## Slide 25: Estimated statistics of applied motion – for all trees

## Slide 26: Estimated statistics of applied motion – for all trees

## Slide 27: Point Spread Function

## Slide 28: Range Spectra

## Slide 29: Qualitative change in images
Gaussian
Sinc, eta = 1.0

## Slide 30: Range Spectra for different baselines

## Slide 31: Adding a DEM
Read in and error checking of external DEM file
Resize/Resample to simulation coordinates
Create Shadow Map for direct scattering

## Slide 32: Example (Direct scattering only)
No DEM
With DEM
HH backscatter
HH backscatter
0.17m wrap
40m wrap
0m wrap
20m wrap
Backscatter
DEM
Shadow Map

## Slide 33: Adding thermal noise
Add a random number to each pixel of every stack, such that

## Slide 34: Backscatter Intensity
-25dB NESZ
-30dB NESZ
-35dB NESZ
-40dB NESZ
-45dB NESZ

## Slide 35: Direct Ground Scattering, the math
Facet surface normal and unit look vector

## Slide 36: Scattering from a cylinder
Each branch is simulated as either an infinite or a finite cylinder based on a flag (by default set to simulate an infinite cylinder)
In case the cylinder is finite
  Karam, Fung and Antar, “Electromagnetic Wave Scattering from Some Vegetation Samples”, TGRS 1988
  Uses generalized Rayleigh-Gans (GRG) Approximation:

## Slide 37: Vegetation Permittivity from Moisture, [Ulaby, El-Reyes, 1987]